## Slide 1: DECISION SUPPORT TOOL
Version 9B

## Slide 2: Description
The Decision Support Tool (DST) is a tool for planning, public works and transportation professionals to integrate health and equity into land use decisions to promote safe, walkable, bikeable, and connected communities.
The DST uses a three-step process to identify recommendations for a specific geographic area.
  Step 1 uses secondary data related to health, equity, active transport, crashes, land use features, and connectivity to assess an area’s existing needs.
  Step 2 uses secondary data and built environment audits to assess an area’s existing walking and biking infrastructure.
  Results from Steps 1 and 2 yield recommendations for how to modify the area to promote walking and biking, including recommendations related to traffic calming, visibility, crosswalks and signalized intersections, bicycle and pedestrian connectivity, asset management, and aesthetics.
  In general, the higher an area’s existing need and the less the area is conducive to walking and biking, the more the recommendations aim to promote active transport.

## Slide 3: Disclaimer
Disclaimer: This Decision Support Tool relies on external sources of information, data, and analysis. The accuracy, recency, and availability of this information, data, and analysis depends on the organizations that maintain them. DST sources should be periodically verified and the DST updated to reflect any changes.

## Slide 4: Instructions
The Big Picture
The purpose of this Decision Support Tool is to consider health when assessing, designing, and building land use projects.
Step 1 of this Tool considers active transportation, equity, crashes, land use, and connectivity. Step 2 assesses existing infrastructure. Step 3 provides recommendations that take health into account.
Using the Tool
Before using this tool, please identify a specific geographic area for a land use project.
Next, complete Steps 1 and 2, which involve gathering information through a series of questions.
Finally, use the information collected through Steps 1 and 2 to select project recommendations in Step 3 that take health into account.
User Tips
Steps 1 & 2 use many existing data sources available online.
  Many of these websites are easiest to use by inputting a specific address. Select an address within the project area for this purpose. Selecting an address somewhere in the middle of the project area would be helpful.
  If a project encompasses more than one geographic unit of analysis (e.g. Census Tract or block group), answer questions for each involved unit independently. Then, average the answers to compute final points.
In Step 3, use the scores calculated in Steps 1 & 2 to determine whether the project should be designed and implemented using recommendations that are “good,” “better,” or “best” for promoting health.
This tool recognizes that projects are unique. As a result, if choosing not to pursue the recommendation contained in the tool, briefly explain why.

## Slide 5: Substantive Changes from V8 to V9
Topic | Changes
Overall | Added disclaimer language about sources and possible changes. Added a description of the DST. Included a spot for a test address in the header of Step 1. Added to instructions language: “Selecting an address somewhere in the middle of the project area would be helpful.”
S1Q1 | Explained in the instructions that If the result is a decimals of .5 or over, the user should round up and if it’s smaller than .5 the user should round down.
S1Q2 | Changed “key” to “legend” for clarify.
S1Q3 | Changed “key” to “legend” for clarify.
S1Q4 | Moved the arrow to the last icon. Moved each image under the corresponding description.
S1Q6 | Replaced “ArcGIS Online map” with “ArcGIS Online Map Viewer.” Changed language to clarify that if the project area straddles multiple color-coded zones, calculate the average. If this average is a whole number, the points assigned should be the average of the two values associated with that whole number.
S1Q8 | Corrected language to indicate that the address for the project area should be input into the “left” corner rather than “right” corner.
S1Q11 & S1Q12 | Replaced use of “Transportation Trails” and ”RTC Bike Trails on Streets” with ”Bike Streets” and changed data source to access ”Bike Streets” map. Deleted S1Q12 based on feedback. Doubled the point-value of S1Q11.
S2Q1 | Replaced “under” with “next to” in instructions. Replaced “ArcGIS Online map” with “ArcGIS Online Map Viewer” in instructions.
S2Q2 | Updated link with new mapping tool created by RTC. Updated question wording and instructions to explain use of RTC mapping tool.
S2Q3 | Clarified that “MAPS Mini Score” used should be points rather than percentage. Clarified that the MAPS assessment should be conducted at the block-level.

## Slide 6: Substantive Changes from V8 to V9
Topic | Changes
Overall | Clarified that if a recommendation is not pursued, the user should explain and document why the recommendation is not appropriate.
Traffic Calming | Replaced “chokers” with “curb extensions” under “Best”
Crosswalk and signalized intersections | Changed “Install overhead pedestrian activated (sensors) flashers or signals” to “Install pedestrian activated (sensors) flashers or signals” under ”Best.” Changed “Install signal timing to utilize exclusive pedestrian phase and/or pedestrian scramble” to “Install signal timing to utilize exclusive pedestrian phase” under “Best.”
Bicycle Improvements | Changed “Install painted bike boxes at intersections” to “Install bike boxes at intersections using paint or other materials” under “Better.” Changed “Add occasional green bike symbols” to “Add green bike legend panels” under “Better.”
Visibility | Changed “Remove all utility boxes out of sight lines” to ”Ensure that all utilities are out of sight lines” under “Better” and “Best.”

## Slide 7
Step 1: Assess area’s existing need
Step 2: Assess existing infrastructure
Step 3: Select proposed infrastructure
 | Below Average | Average | Above Average
High | Best | Best | Best
Medium | Best | ≥ Better | ≥ Good
Low | ≥ Better | ≥ Good | Minimal potential for benefit
Existing Infrastructure
Area Existing Need
Roadmap

## Slide 8
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q1: How underserved is the geographic area where the project will be built? use U. of Wisconsin Area Deprivation Index (state deciles), available here: https://www.neighborhoodatlas.medicine.wisc.edu/mapping ADI (least disadvantaged) (most disadvantaged) ADI & Points: 1 2 3 4 5 6 7 8 9 10 | Equity | /10
S1Q2: What is the current rate of biking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-.3% .4-1.2% 1.3-2.5% 2.6-4.3% 4.9-7.1% Points: 1 2 3 4 5 | Active transport | /5
S1Q3: What is the current rate of walking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-1.7% 1.8-5% 5.4-11% 13.6-22.5% 45.3-57.6% Points: 1 2 3 4 5 | Active transport | /5
S1Q4: What is the pedestrian crash density in the area? (pedestrian crashes/sq. mile) (use NDOT map, available here) Crashes: 0-8 9-16 17-27 28-47 48+ Points: 1 2 3 4 5 | Crash | /5
S1Q5: What is the bicycle crash density in the area? (bicycle crashes/sq. mile) (use NDOT map, available here) Crashes: 0-4 5-7 8-10 11-15 15+ Points: 1 2 3 4 5 | Crash | /5
S1Q6: What is the land use diversity index? (jobs to housing) (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Diversity: 0-2 2-3 3-4 4-5 5-6 6-7 7-8 8-9 9-10 Points: 1 1.5 2 2.5 3 3.5 4 4.5 5 | Land Use | /5
Test Address: _________________________________________________________________

## Slide 9: S1Q1 Instructions
Click the link provided for the U. of Wisconsin Area Deprivation Index (ADI), available here.
Select Nevada
Ensure “State-Only Deciles” is selected (this is the default)
Enter the test address located within the project area.
Select “Search”
A State Decile Information box will appear. Use this for the ADI value AND the point value.
  If the project area straddles multiple state decile values, average them.
  Round decimal of .5 or more up to the next whole number and decimals under .5 down.
Place the value, between 1 and 10 in the “Pts” column

## Slide 10
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q1: How underserved is the geographic area where the project will be built? use U. of Wisconsin Area Deprivation Index (state deciles), available here: https://www.neighborhoodatlas.medicine.wisc.edu/mapping ADI (least disadvantaged) (most disadvantaged) ADI & Points: 1 2 3 4 5 6 7 8 9 10 | Equity | /10
S1Q2: What is the current rate of biking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-.3% .4-1.2% 1.3-2.5% 2.6-4.3% 4.9-7.1% Points: 1 2 3 4 5 | Active transport | /5
S1Q3: What is the current rate of walking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-1.7% 1.8-5% 5.4-11% 13.6-22.5% 45.3-57.6% Points: 1 2 3 4 5 | Active transport | /5
S1Q4: What is the pedestrian crash density in the area? (pedestrian crashes/sq. mile) (use NDOT map, available here) Crashes: 0-8 9-16 17-27 28-47 48+ Points: 1 2 3 4 5 | Crash | /5
S1Q5: What is the bicycle crash density in the area? (bicycle crashes/sq. mile) (use NDOT map, available here) Crashes: 0-4 5-7 8-10 11-15 15+ Points: 1 2 3 4 5 | Crash | /5
S1Q6: What is the land use diversity index? (jobs to housing) (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Diversity: 0-2 2-3 3-4 4-5 5-6 6-7 7-8 8-9 9-10 Points: 1 1.5 2 2.5 3 3.5 4 4.5 5 | Land Use | /5

## Slide 11: S1Q2 Instructions
Click the link for U.S. Census Data on biking to work, available here.
Select “Table” and on the left-hand panel under “Selection Map” select “Commuting Characteristics by Sex” and then select “Table” once more
  Use “Geographies” and select “Tract”, “Nevada”, “Clark County, NV”, “All Census Tracts in Clark County” and close.
  Select “Map”
  Be sure to use the most current time period for which data is available
Zoom in to approximate the project area
Use the legend to identify the rate percentile of biking to work
  Be sure to identify the rate percentile, not the Census Tract
  If project area straddles multiple percentile groups (i.e. is in multiple Tracts), take the average
Assign and record the corresponding points

## Slide 12
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q1: How underserved is the geographic area where the project will be built? use U. of Wisconsin Area Deprivation Index (state deciles), available here: https://www.neighborhoodatlas.medicine.wisc.edu/mapping ADI (least disadvantaged) (most disadvantaged) ADI & Points: 1 2 3 4 5 6 7 8 9 10 | Equity | /10
S1Q2: What is the current rate of biking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-.3% .4-1.2% 1.3-2.5% 2.6-4.3% 4.9-7.1% Points: 1 2 3 4 5 | Active transport | /5
S1Q3: What is the current rate of walking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-1.7% 1.8-5% 5.4-11% 13.6-22.5% 45.3-57.6% Points: 1 2 3 4 5 | Active transport | /5
S1Q4: What is the pedestrian crash density in the area? (pedestrian crashes/sq. mile) (use NDOT map, available here) Crashes: 0-8 9-16 17-27 28-47 48+ Points: 1 2 3 4 5 | Crash | /5
S1Q5: What is the bicycle crash density in the area? (bicycle crashes/sq. mile) (use NDOT map, available here) Crashes: 0-4 5-7 8-10 11-15 15+ Points: 1 2 3 4 5 | Crash | /5
S1Q6: What is the land use diversity index? (jobs to housing) (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Diversity: 0-2 2-3 3-4 4-5 5-6 6-7 7-8 8-9 9-10 Points: 1 1.5 2 2.5 3 3.5 4 4.5 5 | Land Use | /5

## Slide 13: S1Q3 Instructions
Click the link for U.S. Census Data on biking to work, available here.
Select “Table” and on the left-hand panel under “Selection Map” select “Commuting Characteristics by Sex” and then select “Table” once more
  Use “Geographies” and select “Tract”, “Nevada”, “Clark County, NV”, “All Census Tracts in Clark County” and close.
  Select “Map”
Zoom in to approximate the project area
Use the legend to identify the rate percentile of walking to work
  If project area straddles multiple percentile groups, take the average
Assign and record the corresponding points

## Slide 14
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q1: How underserved is the geographic area where the project will be built? use U. of Wisconsin Area Deprivation Index (state deciles), available here: https://www.neighborhoodatlas.medicine.wisc.edu/mapping ADI (least disadvantaged) (most disadvantaged) ADI & Points: 1 2 3 4 5 6 7 8 9 10 | Equity | /10
S1Q2: What is the current rate of biking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-.3% .4-1.2% 1.3-2.5% 2.6-4.3% 4.9-7.1% Points: 1 2 3 4 5 | Active transport | /5
S1Q3: What is the current rate of walking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-1.7% 1.8-5% 5.4-11% 13.6-22.5% 45.3-57.6% Points: 1 2 3 4 5 | Active transport | /5
S1Q4: What is the pedestrian crash density in the area? (pedestrian crashes/sq. mile) (use NDOT map, available here) Crashes: 0-8 9-16 17-27 28-47 48+ Points: 1 2 3 4 5 | Crash | /5
S1Q5: What is the bicycle crash density in the area? (bicycle crashes/sq. mile) (use NDOT map, available here) Crashes: 0-4 5-7 8-10 11-15 15+ Points: 1 2 3 4 5 | Crash | /5
S1Q6: What is the land use diversity index? (jobs to housing) (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Diversity: 0-2 2-3 3-4 4-5 5-6 6-7 7-8 8-9 9-10 Points: 1 1.5 2 2.5 3 3.5 4 4.5 5 | Land Use | /5

## Slide 15: S1Q4 Instructions
Click on the link for the Nevada Department of Transportation Crash Data 2015-2017 map, available here.
Enter an address within the project area and click “Search.”
Select the “Screening” tool icon.
Under “Search Address,” re-enter the address in “Search for a Location.”
Under “Show Results Within,” enter 0.25 miles for Buffer distance; a red circle with a .25 mile radius will appear around the address.
Click “Draw an Area” and select draw mode “POLYLINE.”
Use the POLYLINE tool to draw a line along the project area. Right click an area on the map to begin drawing. Right click at the end of each segment to continue drawing. Double-click to complete drawing.

## Slide 16: S1Q4 Instructions - Continued
Click “Report” inside the “Screening” toolbox.
Under “Choose units of analysis,” select “Square Miles” and “Miles.”
In the “Filter” section, select “Pedestrian.”
  In the “Crash Count” section beneath the title, note the “Number of Crashes in Current Extent.”
  Divide this number of crashes by the Area in mi² for the buffer zone.
  Round to the nearest whole number
Record the calculated points

## Slide 17
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q1: How underserved is the geographic area where the project will be built? use U. of Wisconsin Area Deprivation Index (state deciles), available here: https://www.neighborhoodatlas.medicine.wisc.edu/mapping ADI (least disadvantaged) (most disadvantaged) ADI & Points: 1 2 3 4 5 6 7 8 9 10 | Equity | /10
S1Q2: What is the current rate of biking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-.3% .4-1.2% 1.3-2.5% 2.6-4.3% 4.9-7.1% Points: 1 2 3 4 5 | Active transport | /5
S1Q3: What is the current rate of walking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-1.7% 1.8-5% 5.4-11% 13.6-22.5% 45.3-57.6% Points: 1 2 3 4 5 | Active transport | /5
S1Q4: What is the pedestrian crash density in the area? (pedestrian crashes/sq. mile) (use NDOT map, available here) Crashes: 0-8 9-16 17-27 28-47 48+ Points: 1 2 3 4 5 | Crash | /5
S1Q5: What is the bicycle crash density in the area? (bicycle crashes/sq. mile) (use NDOT map, available here) Crashes: 0-4 5-7 8-10 11-15 15+ Points: 1 2 3 4 5 | Crash | /5
S1Q6: What is the land use diversity index? (jobs to housing) (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Diversity: 0-2 2-3 3-4 4-5 5-6 6-7 7-8 8-9 9-10 Points: 1 1.5 2 2.5 3 3.5 4 4.5 5 | Land Use | /5

## Slide 18: S1Q5 Instructions
Click on the link for the Nevada Department of Transportation Crash Data 2015-2017 map, available here.
Enter an address within the project area and click “Search.”
Select the “Screening” tool icon.
Under “Search Address,” re-enter the address in “Search for a Location.”
Under “Show Results Within,” enter 0.25 miles for Buffer distance; a red circle with a .25 mile radius will appear around the address.
Click “Draw an Area” and select draw mode “POLYLINE.”
Use the POLYLINE tool to draw a line along the project area. Right click an area on the map to begin drawing. Right click at the end of each segment to continue drawing. Double-click to complete drawing.

## Slide 19: S1Q5 Instructions - Continued
Click “Report” inside the “Screening” toolbox.
Under “Choose units of analysis,” select “Square Miles” and “Miles.”
In the “Filter” section, select “Bicycle.”
  In the “Crash Count” section beneath the title, note the “Number of Crashes in Current Extent.”
  Divide this number of crashes by the Area in mi² for the buffer zone.
  Round to the nearest whole number
Record the calculated points

## Slide 20: S1Q5 Instructions - Continued
Select Report inside the Screening toolbox.
  Click on the gear icon (Choose units for analysis).
  Under Show area results in, use the tab down menu to select Square Miles.
  Ensure the tab down menu for Show length results in is set to Feet.
  Note the Area will change from square ft (ft²) to square miles (mi²); use the area in mi² for calculations.
Under the Filter section, click on the tab to select Bicycle.
  In the Crash Count section beneath the title, Number of Crashes in Current Extent, note the number of crashes.
  Divide the number of crashes by the Area in square miles for the buffer zone.
  Round to the nearest whole number as necessary
  Place the calculated Point value in the “Pts” column.

## Slide 21
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q1: How underserved is the geographic area where the project will be built? use U. of Wisconsin Area Deprivation Index (state deciles), available here: https://www.neighborhoodatlas.medicine.wisc.edu/mapping ADI (least disadvantaged) (most disadvantaged) ADI & Points: 1 2 3 4 5 6 7 8 9 10 | Equity | /10
S1Q2: What is the current rate of biking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-.3% .4-1.2% 1.3-2.5% 2.6-4.3% 4.9-7.1% Points: 1 2 3 4 5 | Active transport | /5
S1Q3: What is the current rate of walking to work in the proposed project’s Census Tract? (use U.S. Census data, available here) Rate: 0-1.7% 1.8-5% 5.4-11% 13.6-22.5% 45.3-57.6% Points: 1 2 3 4 5 | Active transport | /5
S1Q4: What is the pedestrian crash density in the area? (pedestrian crashes/sq. mile) (use NDOT map, available here) Crashes: 0-8 9-16 17-27 28-47 48+ Points: 1 2 3 4 5 | Crash | /5
S1Q5: What is the bicycle crash density in the area? (bicycle crashes/sq. mile) (use NDOT map, available here) Crashes: 0-4 5-7 8-10 11-15 15+ Points: 1 2 3 4 5 | Crash | /5
S1Q6: What is the land use diversity index? (jobs to housing) (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Diversity: 0-2 2-3 3-4 4-5 5-6 6-7 7-8 8-9 9-10 Points: 1 1.5 2 2.5 3 3.5 4 4.5 5 | Land Use | /5

## Slide 22: S1Q6 Instructions
Click on the link provided for the U.S. Environmental Protection Agency (EPA) Smart Location database; available here.
Under “View In,” select “ArcGIS Online Map Viewer”
Enter the address for project area inside the text box on the top right.
On the left, click on “Basemap” and select “Imagery Hybrid.”
Click on “Details” in the top left and then click on “Content.”
Click on the right-pointing arrow next to “Smart Location Database” to reveal the drop-down menu.
Check the the “Land use diversity” tab box. The map will adjust to show a color-coded view of the data.
Click on “Legend” in the top left. Cross-reference color(s) in the project area with the color/number range in the map key.
  If the project area straddles multiple color-coded zones, calculate the average. If this average is a whole number, the points assigned should be the average of the two values associated with that whole number.
Record the corresponding points.

## Slide 23
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q7: How many housing units + jobs per acre in the area? (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Density: 0-10 10-25 25-50 50-100 100+ Points: 1 2 3 4 5 | Land Use | /5
S1Q8: How many schools (CCSD, private, or charter) are in the area and within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q9: How many public parks are in the project area or within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q10: How many bus stops are within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 or more Points: 0 2 | Connectivity | /2
S1Q11: How many bike streets are in the area or within ¼ mile radius? (bike streets: use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/) Number: 0 1 >1 Points: 0 2 4 | Connectivity | /4
Step 1 Points 0-17 points: Low Need 18-32 points: Medium Need 33-50: High Need |  | /50

## Slide 24: S1Q7 Instructions
Click on the link provided for the U.S. Environmental Protection Agency (EPA) Smart Location database; available here.
Under “View In,” select “ArcGIS Online map”
Enter the address for project area inside the text box on the top right.
On the left, click on “Basemap” and select “Imagery Hybrid.”
Click on “Details” in the top left and then click on “Content.”
Click on the right-pointing arrow next to “Smart Location Database” to reveal the drop down menu.
Check the the “Activity Density” tab box. The map will adjust to show a color-coded view of the data.
Click on “Legend” in the top left. Cross-reference color(s) in the project area with the color/number range in the map key.
  If the project area straddles multiple color-coded zones, calculate the average.
Record the corresponding points.

## Slide 25
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q7: How many housing units + jobs per acre in the area? (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Density: 0-10 10-25 25-50 50-100 100+ Points: 1 2 3 4 5 | Land Use | /5
S1Q8: How many schools (CCSD, private, or charter) are in the area and within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q9: How many public parks are in the project area or within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q10: How many bus stops are within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 or more Points: 0 2 | Connectivity | /2
S1Q11: How many bike streets are in the area or within ¼ mile radius? (bike streets: use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/) Number: 0 1 >1 Points: 0 2 4 | Connectivity | /4
Step 1 Points 0-17 points: Low Need 18-32 points: Medium Need 33-50: High Need |  | /50

## Slide 26: S1Q8 Instructions
Click on the link for the City of Las Vegas GeoView data, available here.
Enter the address for project area inside the text box in the top left corner.
Click on “Layers” under the address bar.
Click on the right-pointing arrow next to “Community Services.”
Check the following boxes: “CCSD Schools,” “Charter Schools,” & “Private Schools”
Click on “Legend”
Review the map symbols for each selection. This key will show how each selection is displayed on the interactive web map.
Zoom in and out as needed to see all schools within ½ mile.
Measurement Steps:
  Select the ruler icon for the “Measure Tool” in the top right corner. A window will pop-up with instructions for using it.
  Change the unit of measurement in the text box that says “Length” to “Miles.”
  For each CCSD, charter, and private school use the “Measure tool” to see how far the school is from the closest edge of the project.
  Note the total number of CCSD, charter, and private schools within ½ mile.
  Record the associated points.
  Click on the ‘X’ icon (above), select the Toggle Sidebar and the “Layers/Legend” menu will re-appear.

## Slide 27
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q7: How many housing units + jobs per acre in the area? (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Density: 0-10 10-25 25-50 50-100 100+ Points: 1 2 3 4 5 | Land Use | /5
S1Q8: How many schools (CCSD, private, or charter) are in the area and within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q9: How many public parks are in the project area or within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q10: How many bus stops are within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 or more Points: 0 2 | Connectivity | /2
S1Q11: How many bike streets are in the area or within ¼ mile radius? (bike streets: use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/) Number: 0 1 >1 Points: 0 2 4 | Connectivity | /4
Step 1 Points 0-17 points: Low Need 18-32 points: Medium Need 33-50: High Need |  | /50

## Slide 28: S1Q9 Instructions
Click on the link for the City of Las Vegas GeoView data, available here.
Enter the address for project area inside the text box in the top right corner.
Click on “Layers” under the address bar.
Click on the right-pointing arrow next to “Community Services.”
Check the the “Parks” box
Click on “Legend”
Review the map symbols for each selection. This key will show how each selection is displayed on the interactive web map.
Zoom in and out as needed to see all parks within ½ mile.
Measurement Steps:
  Select the ruler icon for the “Measure Tool” in the top right corner. A window will pop-up with instructions for using it.
  Change the unit of measurement in the text box that says “Length” to “Miles.”
  For each park use the “Measure tool” to see how far the park is from the closest edge of the project.
  Note the total number of parks within ½ mile.
  Record the associated Points.
  Click on the ‘X’ icon (above), select the Toggle Sidebar and the “Layers/Legend” menu will re-appear.

## Slide 29
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q7: How many housing units + jobs per acre in the area? (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Density: 0-10 10-25 25-50 50-100 100+ Points: 1 2 3 4 5 | Land Use | /5
S1Q8: How many schools (CCSD, private, or charter) are in the area and within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q9: How many public parks are in the project area or within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q10: How many bus stops are within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 or more Points: 0 2 | Connectivity | /2
S1Q11: How many bike streets are in the area or within ¼ mile radius? (bike streets: use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/) Number: 0 1 >1 Points: 0 2 4 | Connectivity | /4
Step 1 Points 0-17 points: Low Need 18-32 points: Medium Need 33-50: High Need |  | /50

## Slide 30: S1Q10 Instructions
Click on the link for the City of Las Vegas GeoView data, available here.
Enter the address for project area inside the text box in the top right corner.
Click on “Layers” under the address bar.
Click on the right-pointing arrow next to “Transportation.”
Check the following boxes: “RTC Bus Stops”
Click on “Legend”
Review the map symbols for each selection. This key will show how each selection is displayed on the interactive web map.
Zoom in and out as needed to see all RTC Bus Stops within ½ mile.
Measurement Steps:
  Select the ruler icon for the “Measure Tool” in the top right corner. A window will pop-up with instructions for using it.
  Change the unit of measurement in the text box that says “Length” to “Miles.”
  Note the total number of RTC Bus Stops within ½ mile. Use the “Measure tool” if needed.
  Record the associated Points.
  Click on the ‘X’ icon (above), select the Toggle Sidebar and the “Layers/Legend” menu will re-appear.

## Slide 31
Step 1: Assess the area’s need
Existing needs assessment | Domain | Pts
S1Q7: How many housing units + jobs per acre in the area? (use EPA Smart Location database (c. 2010), available here: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer) Density: 0-10 10-25 25-50 50-100 100+ Points: 1 2 3 4 5 | Land Use | /5
S1Q8: How many schools (CCSD, private, or charter) are in the area and within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q9: How many public parks are in the project area or within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 >1 Points: 0 1 2 | Connectivity | /2
S1Q10: How many bus stops are within ½ mile radius? (use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/#) Number: 0 1 or more Points: 0 2 | Connectivity | /2
S1Q11: How many bike streets are in the area or within ¼ mile radius? (bike streets: use City of Las Vegas data, available here: https://geoview-lasvegasnevada-gov.appspot.com/) Number: 0 1 >1 Points: 0 2 4 | Connectivity | /4
Step 1 Points 0-17 points: Low Need 18-32 points: Medium Need 33-50: High Need |  | /50

## Slide 32: S1Q11 Instructions
Click on the link for the City of Las Vegas GeoView data, available here.
Enter the address for project area inside the text box in the top left corner.
Click on “Layers” under the address bar.
Click on the right-pointing arrow next to “Transportation.”
Check “Bike Streets.”
Click on “Legend”
Count and record the number of existing bike streets in the project area or within ¼ mile buffer.
Zoom in and out as needed to see all bike streets within ¼ mile.
Measurement Steps:
  Select the ruler icon for the “Measure Tool” in the top right corner. A window will pop-up with instructions for using it.
  Change the unit of measurement in the text box that says “Length” to “Miles.”
  Use the “Measure Tool” to see how far the bike street is from the closest edge of the project.
  Note the total number of bike streets within ¼ mile.
  Record the associated points.
  Click on the ‘X’ icon (above), select the Toggle Sidebar and the “Layers/Legend” menu will re-appear.

## Slide 33
Step 1: Assess area’s existing need
 | Below Average | Average | Above Average
High | Best | Best | Best
Medium | Best | ≥ Better | ≥ Good
Low | ≥ Better | ≥ Good | Minimal potential for benefit
Existing Infrastructure
Area Existing Need
Assess Existing Need
Add up all the points for Step 1 to determine if need is “High,” “Medium,” or “Low”

## Slide 34
Step 2: Assess existing infrastructure
Existing infrastructure | Pts
S2Q1: What is the National Walkability Index Score? use EPA National Walkability Score, available here: https://geodata.epa.gov/arcgis/rest/services/OA/WalkabilityIndex/MapServer Index: 1-5.75 5.76-10.5 10.51-15.25 15.26-20 Points: 3.125 6.25 9.375 12.5 | /12.5
S2Q2: What is the level of comfort on the closest collector or arterial roadway segment(s)? (use RTC Ped/Bike Plan Level of Comfort Online Tool,, available here: https://rtcsnv.maps.arcgis.com/apps/webappviewer/index.html?id=f3ee5b445fdf48d18e6969ef106c5e09) Comfort: Level 4 Level 3 Level 2 Level 1 Points: 3.125 6.25 9.375 12.5 | /12.5
S2Q3: What is the average Microscale Audit of Pedestrian Streetscapes (MAPS) mini score for all of the segments in the project area? (conduct MAPS mini for each segment and then average them to get a MAPS mini score. Resources available here: https://drjimsallis.org/measure_maps.html#MAPSMINI. MAPS Mini Score: 0-1 2-3 4-5 6-7 8-9 10-11 12-13 14-15 16-17 18-19 20-21 Points: 0 2.5 5 7.5 10 12.5 15 17.5 20 22.5 25 | /25
Step 2 Points 0-17 points: Below Average 18-32 points: Average 33-50: Above Average | /50

## Slide 35: S2Q1 Instructions
Click the link provided for the U.S. Environmental Protection Agency (EPA) National Walkability Score, available here.
Next to “View In,” select “ArcGIS Online Map Viewer”
Enter the address for project area inside the text box on the top right.
On the left, click on “Basemap” and select “Imagery Hybrid.”
The Index will be color-coded by area.
Select the “Legend” menu.
  For value(s), cross-reference color(s) in the project area with the color/number range in the map key.
  If the project area is straddles multiple color-coded zones in the map view, compute the average.
  Record the corresponding points.

## Slide 36
Step 2: Assess existing infrastructure
Existing infrastructure | Pts
S2Q1: What is the National Walkability Index Score? use EPA National Walkability Score, available here: https://geodata.epa.gov/arcgis/rest/services/OA/WalkabilityIndex/MapServer Index: 1-5.75 5.76-10.5 10.51-15.25 15.26-20 Points: 3.125 6.25 9.375 12.5 | /12.5
S2Q2: What is the level of comfort on the closest collector or arterial roadway segment(s)? (use RTC Ped/Bike Plan Level of Comfort Online Tool,, available here: https://rtcsnv.maps.arcgis.com/apps/webappviewer/index.html?id=f3ee5b445fdf48d18e6969ef106c5e09) Comfort: Level 4 Level 3 Level 2 Level 1 Points: 3.125 6.25 9.375 12.5 | /12.5
S2Q3: What is the average Microscale Audit of Pedestrian Streetscapes (MAPS) mini score for all of the segments in the project area? (conduct MAPS mini for each segment and then average them to get a MAPS mini score. Resources available here: https://drjimsallis.org/measure_maps.html#MAPSMINI. MAPS Mini Score: 0-1 2-3 4-5 6-7 8-9 10-11 12-13 14-15 16-17 18-19 20-21 Points: 0 2.5 5 7.5 10 12.5 15 17.5 20 22.5 25 | /25
Step 2 Points 0-17 points: Below Average 18-32 points: Average 33-50: Above Average | /50

## Slide 37: S2Q2 Instructions
Click on the Existing Level of Comfort for bicycling map tool from the Regional Transportation Commission Regional Bicycle and Pedestrian Plan, available here.
Enter the address for project area inside the address text box in the top left.
Find the closest collector or arterial roadway to the project area with either a green, blue, orange, or red line on the roadway.
  If there is one such line in the project area, record the point value associated with its corresponding level of comfort.
  If there are multiple such line in the project area, average their Levels of Comfort. Round decimal of .5 or more up to the next Level of Comfort and decimals under .5 down.
  If there is no such line in the project area, use the measurement tool, which looks like a ruler, to find the closest one. Record the point value associated with its corresponding level of comfort.

## Slide 38
Step 2: Assess existing infrastructure
Existing infrastructure | Pts
S2Q1: What is the National Walkability Index Score? use EPA National Walkability Score, available here: https://geodata.epa.gov/arcgis/rest/services/OA/WalkabilityIndex/MapServer Index: 1-5.75 5.76-10.5 10.51-15.25 15.26-20 Points: 3.125 6.25 9.375 12.5 | /12.5
S2Q2: What is the level of comfort on the closest collector or arterial roadway segment(s)? (use RTC Ped/Bike Plan Level of Comfort Online Tool,, available here: https://rtcsnv.maps.arcgis.com/apps/webappviewer/index.html?id=f3ee5b445fdf48d18e6969ef106c5e09) Comfort: Level 4 Level 3 Level 2 Level 1 Points: 3.125 6.25 9.375 12.5 | /12.5
S2Q3: What is the average Microscale Audit of Pedestrian Streetscapes (MAPS) mini score for all of the segments in the project area? (conduct MAPS mini for each segment and then average them to get a MAPS mini score. Resources available here: https://drjimsallis.org/measure_maps.html#MAPSMINI. MAPS Mini Score: 0-1 2-3 4-5 6-7 8-9 10-11 12-13 14-15 16-17 18-19 20-21 Points: 0 2.5 5 7.5 10 12.5 15 17.5 20 22.5 25 | /25
Step 2 Points 0-17 points: Below Average 18-32 points: Average 33-50: Above Average | /50

## Slide 39: S2Q3 Instructions
Click the link provided for the MAPS Mini Survey; available here.
Select “MAPS Mini Survey” to open the survey
The “MAPS Mini Protocol” and “MAPS Mini Picture Guide” provides field procedures for data collection with a more in-depth understanding of how to assess segments during the survey for each question.
Complete the “MAPS Mini Survey” for each segment – i.e., block. Average the MAPS Mini points for all segments.
Use the MAPS Mini Points to derive and record the corresponding DST points.
Note: the MAPS Mini Survey may also be completed using online maps, though the information may not be as up-to-date.

## Slide 40
Step 2: Assess existing infrastructure
 | Below Average | Average | Above Average
High | Best | Best | Best
Medium | Best | ≥ Better | ≥ Good
Low | ≥ Better | ≥ Good | Minimal potential for benefit
Existing Infrastructure
Area Existing Need
Assess Existing Infrastructure
Add up all the points for Step 2 to determine if infrastructure is “Below Average,” “Average,” or “Above Average”

## Slide 41
Step 3: Select proposed infrastructure
 | Below Average | Average | Above Average
High | Best | Best | Best
Medium | Best | ≥ Better | ≥ Good
Low | ≥ Better | ≥ Good | Minimal potential for benefit
Existing Infrastructure
Area Existing Need
Select Infrastructure
Based on Steps 1 & 2, determine which set of recommendations to pursue. Place an “X” in the box where the Area Existing Need Score (Step 1 Score) and the Existing Infrastructure Score (Step 2 Score) meet. Then, attempt to integrate each recommendation in the corresponding column during Step 3 Analysis.
Note: Not every infrastructure recommendation is appropriate for every project. If specific infrastructure is not appropriate, explain why in the “N/A” column

## Slide 42
Category | Good for health promotion | Better for health promotion | Best for health promotion | N/A (If a rec is not selected, explain & document why it is not appropriate)
Speed limit | 35 mph | 30 mph | 25 mph | 
Traffic calming | Reduce lane widths with centerlines, edge lines or other pavement markings | Reduce lane widths with raised center medians to discourage passing in two-way turn lanes Install painted curb extensions at crosswalks. Install painted chicanes with lane delineators | Reduce lane widths and/or reduce number of lanes Install raised center medians Install raised curb extensions Install curb extensions and chicanes Install speed warning flashing beacons. | 
Sidewalks | Ensure minimum 4-ft clear width in sidewalk. Repair trip hazards. Verify sidewalks and ramp transitions are PROWAG compliant. | Ensure minimum 5-ft clear width in sidewalk. Repair trip hazards. Verify sidewalks and ramp transitions are PROWAG compliant. Install detached sidewalks. | Install wide sidewalks, preferably 10-ft min. Repair trip hazards. Verify sidewalks and ramp transitions are PROWAG compliant. Install detached sidewalks with parklets. | 
Step 3: Select proposed infrastructure

## Slide 43
Category | Good for health promotion | Better for health promotion | Best for health promotion | N/A (If a rec is not selected, explain & document why it is not appropriate)
Crosswalks & signalized Intersections | Install crosswalk markings, warning signs and yield markings. Install PROWAG- compliant sidewalk ramps and push buttons. Install audible messages at signalized crosswalks and use ped crossing speed of 3.5 ft per second. | Install crosswalk markings, warning signs, and yield markings. Install PROWAG-compliant directional sidewalk ramps and push buttons. Provide PROWAG- compliant directional sidewalk Ramps. Install pedestrian activated flashing beacons. Install median refuge. Install painted curb extensions. Improve lighting at sidewalk ramp and through crosswalks. Install leading ped interval. Install No Right on Red during ped peak hours. | Install pedestrian activated (sensors) flashers or signals. Provide PROWAG compliant directional SW Ramps. Install advanced warning flashers. Shorten crossing distance by installing curb extensions. Install median refuge with Danish offset at mid-block crosswalks. Install pedestrian guide fencing to discourage jaywalking. Install leading ped interval. Reduce walking speed to 3 ft/sec at locations with high numbers of seniors or people with disabilities. Install No Right on red. Eliminate permissive left-turns during pedestrian peak hours. Install signal timing to utilize exclusive pedestrian phase. Install shade structures on corners. | 
Step 3: Select proposed infrastructure

## Slide 44
Category | Good for health promotion | Better for health promotion | Best for health promotion | N/A (If a rec is not selected, explain & document why it is not appropriate)
Bicycle improvements | Install exclusive bike lanes with applicable signs and markings. Install bike racks near commercial businesses. | Install buffered bike lanes with applicable signs and markings. Add green bike legend panels. Install bike boxes at intersections using paint or other materials. Install bike racks near commercial businesses. Consider whether it is possible to extend bike improvements to connect to pre-existing bike infrastructure | Install protected bike lanes with raised barrier and/or physical delineators/posts. Install green bike lane markings through transitions or conflict locations. Install bike signals and bike detectors at signalized intersections. Install wayfinding signs. Install bike lockers near transit stops or commercial hubs. Consider whether it is possible to extend bike improvements to connect to pre-existing bike infrastructure | 
Step 3: Select proposed infrastructure

## Slide 45
Category | Good for health promotion | Better for health promotion | Best for health promotion | N/A (If a rec is not selected, explain & document why it is not appropriate)
Access Management | Reduce the number of driveways and increase driveway spacing. | Install raised center medians to define vehicle ingress and egress locations and turning movements. Upgrade ramps at driveways to PROWAG. | Reduce driveway radius to slow drivers and improve pedestrian visibility. Upgrade ramps at driveways to PROWAG. Require commercial businesses owners to acquire cross-access agreements and share driveways and parking. | 
Visibility | Remove all walls, shrubs, trees, and signs out of sight lines. Install lighting to meet minimum intersection light levels, per Clark County Uniform Standard Drawing (AUSD) 300.S3 | Remove all walls, shrubs, trees, and signs out of sight lines. Ensure that all utilities are out of sight lines. Meet sidewalk illumination light levels of 0.2 FC minimum average along sidewalk Meet minimum pedestrian illuminance level of 2.0 FC minimum average on corners and through entire crosswalk. | Remove all walls, shrubs, trees, and signs out of sight lines. Ensure that all utilities are out of sight lines. Meet high sidewalk illumination light levels of 0.2 FC along sidewalk Meet highest pedestrian illuminance levels of 3.4 FC minimum average on corners and through entire crosswalk. | 
Step 3: Select proposed infrastructure

## Slide 46
Category | Good for health promotion | Better for health promotion | Best for health promotion | N/A (If a rec is not selected, explain & document why it is not appropriate)
Bicycle & pedestrian connectivity | Evaluate project vicinity to nearby pedestrian attractors (parks, retail, schools, trails) and install interim asphalt concrete path(s) connections to corners or existing improvements. | Evaluate project vicinity to nearby pedestrian attractors and install crosswalks, warning signs, sidewalk ramps and AC paths for connectivity. Install shaded bus shelters behind sidewalk. Minimize or eliminate adjacent sawtooths beyond project boundary. | Evaluate projects vicinity to nearby pedestrian attractors, install interim crosswalks and AC paths accordingly, and install permanent improvements, curb, gutter, sidewalk, streetlights, and provide connections to existing bike and pedestrian infrastructure. Install shaded bus shelters behind sidewalk. Fill missing sidewalk gaps with permanent sidewalk and lighting improvements. Consider the possibility of installing permanent improvements beyond project boundary to eliminate sawtooths | 
Aesthetics | Install shade trees. | Install shade trees. Install active wayfinding signage/maps. | Install regularly spaced shade trees, and park benches. Install active wayfinding signage/maps. Install decorative crosswalks. | 
Step 3: Select proposed infrastructure